## Slide 1
Controlling a Vectored
Thrust Aircraft
By Tyler Freitas
ME547 student
University of Washington
Seattle, WA, USA
tfreita@uw.edu
[3]

## Slide 2: Introduction
Existing Aircraft Motion Control
Harrier Jump Jet - Vertical Takeoff and Landing (VTOL)
Examples of Positional Stability Controllers:
  1. Linear-Quadratic Regulator (LQR) [1]
  2. Nonlinear State-Feedback [2]
Harrier Jump Jet Video [3]
https://video-alexanderstreet-com.offcampus.lib.washington.edu/watch/the-harrier-jump-jet/clips/181690
Harrier Jump Jet [3]

## Slide 3: Problem Formulation: Model
Plant:
  Vectored Thrust Aircraft (2D Rigid Body) with 3 thrusters
Input:
  Reaction forces (F1,F2) of the thrusters on the aircraft
Output:
  Aircraft’s Position (X, Y) and Orientation (θ)
Note:
Reaction forces of thrusters are translated to a common intersection point
r is the distance from the aircraft centroid to the thrusters' intersection.
The simulation only covers the Aircraft’s Position (X, Y)
2D Plant Free-Body Diagram
Note: not to scale

## Slide 4: Problem Formulation: Physics
Aerodynamic Forces: (Newton’s 2nd Law, F = ma)
  Lift/Thrust – Thruster Reactions on Aircraft (Newton’s 3rd Law)
  Weight – Aircraft Mass
  Drag – Air Resistance & Thruster Reactions on Aircraft in Drag direction
Assumptions:
  No Air Torque Resistance
  Small Angle Approximation
  Hovering Aircraft
  Same Angles Changes of the Wingtip Thrusters

## Slide 5: Problem Formulation: Physics Cont’d
Mathematical Variables:
F1 - aircraft horizontal reaction
F2 - aircraft vertical reaction
J - moment of inertia
c - damping coefficient
g - acceleration due to gravity
m - aircraft mass
x - aircraft horizontal position
x′ - aircraft horizontal velocity
x′′ - aircraft horizontal acceleration
y - aircraft vertical position
y′ - aircraft vertical velocity
y′′- aircraft vertical acceleration
θ - aircraft angular position
θ′′ - aircraft angular acceleration
r - length from aircraft centroid to thrusters' intersection
Nonlinear Block Diagram
[1]

## Slide 6: Analysis: Nonlinear State Space Model
[1]
More Analysis Variables:
ye - y equilibrium point
xe - x equilibrium point
ze - state-space equilibrium points
Fe - input equilibrium points
A, B, C, D - state-space matrices
ζ - linearized state-space variable
v - linearized state-space input
R - linearized state-space output
z - nonlinear state-space variable
f - time derivative of z
h - nonlinear state-space output
F - nonlinear state-space input

## Slide 7: Analysis: Jacobian Linearization
Linearized State-Space System [1]
Jacobian Matrices [1]
Nonlinear State-Space System & Equilibrium Points [1]

## Slide 8: Analysis: Linearized System Forms
Linearized Block Diagram
Note: u1 = F1 & u2 = F2 (dummy variables)
Linearized State-Space System [1]

## Slide 9: Numerical Analysis & Simulation Parameters
Numerical Analysis Variables:
G1 - Local x transfer function
G2 - Local y transfer function
I - Identity Matrix
u - eigenvectors
λ - eigenvalues
JA, JB , JC , JD - Jordan Form state-space matrices
Vg - Generalized Eigenvectors matrix
β - Similar Transform Variable
∆t - Sampling time
Q - Positive Definite Identity matrix
P - Lyapunov Symmetric Matrix
V - Lyapunov Function
K - State-Feedback Controller Parameter
L - Observer Controller Parameter
Aobs, Bobs, Cobs, Dobs - Observable Canonical matrices
Ad, Bd, Cd, Dd - Discrete state-space matrices
Actrl, Bctrl, Cctrl, Dctrl - Controllable Canonical matrices
Kobs - Observer State-Feedback Parameter
ω - Sampling frequency
Simulation System Parameters

## Slide 10: Eigenvalue & Lyapunov Stability
Eigenvalue Stability
  Multiple Eigenvalues at the origin conclude that the system is not asymptotically stable.
Lyapunov Stability: (Q = I)
  No unique P, thus not asymptotically stable at the equilibrium point.
System Eigenvalues
Eigenvalue equations
Lyapunov Equation
Lyapunov Function

## Slide 11: Jordan Form
Converted Linearized Jacobian Matrices to Jordan Form
Eigenvalues & Generalized Eigenvalues Matrix
Note: β is the Similar Transform Variable

## Slide 12: Transfer functions
Linearized Transfer Function with Poles & Zeros
State-Space System to Transfer Function
Converted Linearized Jacobian Matrices to Transfer Functions
Notes:
1. No Initial conditions
1. F1 is the only input for Local X dynamics
2. F2 is the only input for Local Y dynamics

## Slide 13: Controllable Canonical Form
Converted Linearized Jacobian Matrices to Controllable Canonical Form

## Slide 14: Observable Canonical Form
Converted Linearized Jacobian Matrices to Observable Canonical Form

## Slide 15: Discrete State-Space
Converted Linearized Jacobian Matrices to Discrete State-Space
Eigenvalues of Ad

## Slide 16: State-Feedback Controller
State-Feedback Gain
Desired Closed-Loop State-Feedback Eigenvalues/Poles:
  Complex dominant poles are close to the origin
    Adjacent poles are at least 5x farther from the complex dominant poles
  The real part of these eigenvalues are negative for stability
Added a State-Feedback Controller to Controllable Canonical Form
Note: Local X has a similar Block Diagram
State-Feedback Controller Block Diagram for Local Y
Note: Same K for Local X & Y responses

## Slide 17: Observer State-Feedback Control
Added an Observer State-Feedback Controller to the Jacobian Matrices
Desired Closed-Loop Observer Eigenvalues/Poles:
  First Observer pole is at least 5x farther from the farthest State-Feedback pole
  Have complex dominant poles
    Observer adjacent poles are 5x farther from its complex dominant poles
  The real part of these eigenvalues are negative for stability
  Poles are far away from the origin for faster dynamics
Same Closed-Loop State-Feedback Eigenvalues

## Slide 18: Results: State-Feedback Step/Impulse

## Slide 19: Results: State-Feedback High/Low Freq. Sine

## Slide 20: Results: Observer State-Feedback Step/Impulse
Note: Plant and Observer have no initial conditions, therefore the responses are the same.

## Slide 21: Results: Observer State-Feedback High/Low Freq. Sine
Note: Plant and Observer have no initial conditions, therefore the responses are the same.

## Slide 22: Conclusion
Linearized State-Feedback & Observer State-Feedback Controller Results:
  Step/Impulse: Converge to a Steady-State Value
  Low & High Frequency: Converge to an Equilibrium Mean
Note: The Model neglected Air Torque Resistance but maintained controllability
Future Improvements:
  Simulating Vertical Takeoff and Landing Maneuvers & External Disturbances Inputs
  Implementing Nonlinear State-Feedback & Observer Controllers

## Slide 23: References
[1] K. J. Åström, R. M. Murray, \textit{Feedback Systems: An Introduction for Scientists and Engineers.} Princeton University Press, 2008. [Online]. Available: http://www.cds.caltech.edu/~murray/books/AM08/pdf/fbs-public\_24Jul2020.pdf. Accessed: Feb. 10, 2024.
[2] C. S. Huang and K. Yuan.“Output Tracking of a Non-Linear Non-Minimum Phase PVTOL Aircraft Based on Non-Linear State Feedback Control”, International Journal of Control, vol. 75, no. 6, pp. 466–473, 2002. Accessed on: March 7, 2024. [Online]. Available: doi:10.1080/00207170210121907.
[3] D. Sharam, W. Gibbs, World Wide Entertainment, The Harrier Jump Jet. (2006). Accessed: Feb. 18, 2024. [Online Video]. Available: https://video.alexanderstreet.com/watch/the-harrier-jump-jet.